We can first start by using static tools to look for issues I used the 2 below

Using cppcheck --enable=all --suppress=missingIncludeSystem main.c 2>err.txt
and flawfinder main.c >>err2.txt

* err.txt will say that on line 23 gets an Obsolete function is called and you should use fgets and not gets

on line 21 the compiler does not like the % on its own
not a security issue but I don't like compiler errors so I changed it to %%

err2.txt says that gets should not be used and that on line 15 the char buffer is not properly restricted this could be a overflow issue it also says that that on line 24 that getchar should check for the buffer bounds when used in a loop

after using the tools I can also look at the src and do dynamic testing to look for issues

line 28 uses scanf(); this is a buffer overflow issue use fgets or getchar
line 20 uses a infinite loop with no exit condition
all operations use int arrays this can be problematic and be overflowed
you are also at risk of integer overflow so you should use a safeint
that same can be said about the double result variable
line 26 getchar has a return type and it is not looked at or stored in a variable